## Slide 1: On the way to a world-competitive fission fragment facility at SARAF
Israel Mardor1,2, Timo Dickel3,4, Leo Weissman1
1Soreq NRC, Yavne, Israel
2Tel Aviv University, Tel Aviv, Israel
3Justus-Liebig-Universität Gießen, Gießen, Germany
4GSI, Darmstadt, Germany
SMI2019, Montreal QC, Canada, July 15th-19th

## Slide 2: Outline
Overview of SARAF and Liquid-Lithium target (LiLiT)
SARAF + Liquid target+ Ion Catcher:
  High rate n-rich isotope generation via neutron induced fission

## Slide 3
Our geographical location
Soreq NRC, Yavne
Montreal – Tel Aviv: ~8,800 km, ~11 hours flight
Notes: Zooming in you can get a better idea of our geographical location. The distance between the Venue and Soreq NRC is 30 km.

## Slide 4: SARAF – Soreq Applied Research Accelerator Facility
To enlarge the experimental nuclear science infrastructure and promote research in Israel
To develop and produce radioisotopes for bio-medical applications
To modernize the source of neutrons at Soreq and extend neutron based research and applications
Notes: 4

## Slide 5: SARAF concept and top level requirements
2) nuclear reaction
[3] radiation and isotopes
1) fast particles
3) applications
SARAF-I: to characterize and proof novel acceleration technologies
OLD initial Phase-II design [1] 30 m long accelerator
[2] target
Parameter | Value | Comment
Ion Species | Protons/Deuterons | M/q ≤ 2
Energy Range | 5 – 40 MeV | Variable energy
Current Range | 0.04 – 5 mA | CW (and pulsed)
Maintenance | Hands-On | Very low beam loss
In operation since 2009
NEW lattice under design
Planned for 2023
SARAF-II linac N. Pichoff et al. IPAC 2017

## Slide 6: Target Hall (2022)
 Phase-I accelerator
2001 2010
Reactor alternative 2014-2023
2014 2022
Phase-II accelerator
diffractometer
Radiopharmaceutical
Thermal n source
40 m
radiography
R&D
SARAF II 2023
Basic Research
Phase I Target Room
2016-2018
GaIn Beam
Dump
2018-2022
Notes: 6

## Slide 7: SARAF I (and the SARAF II area)
SARAF II construction area

## Slide 8
Commissioning
A. Nagler, Linac 2006 K. Dunkel, PAC 2007 C. Piel, PAC 2007 C. Piel, EPAC 2008 A. Nagler, Linac 2008 J. Rodnizki, EPAC 2008 J. Rodnizki, HB 2008 I. Mardor, PAC 2009 A. Perry, SRF 2009 I. Mardor, SRF 2009 L. Weissman, DIPAC 2009 L. Weissman, Linac 2010
Operation
D. Berkovits, Linac 2012 L. Weissman, RuPAC 2012 A. Kreisel, Linac 2014 L. Weissman, WAO 2014 L. Weissman, JINST 2014 L. Weissman, JINST 2015
… see therein several contributions regarding components design, upgrades and developments
 | MeV | mA
p | 4 | 1 CW
p | 2 | 2 CW
d | 5.6 | 1 (10%)
d | 2.6 | 1.1 CW
SARAF-I on site collaboration with Research Instruments (formerly Accel Instruments)

## Slide 9
peak power areal density: ̴ 2.5 kW/cm2
peak power volume density protons: ̴ 0.5 MW/cm3
peak power volume density electrons: ̴ 2 MW/cm3
S. Halfon et al., RSI 84, 123507 (2013)
S. Halfon et al., RSI 85, 056105 (2014)
S. Halfon et al., ARI 106, 57 (2015)
Incident beam power: ̴2-3 kW
Ip = 1-2 mA, 1.91 MeV
In < 3 - 5 × 1010 n/s
18 mm
Thanks to J. Nolen, C. Reed & Y. Momozaki (ANL)
for the help with design and training
Liquid Lithium Target (LiLiT) overview
SARAF I
Notes: 9

## Slide 10
Windowless
1.91 MeV
1-2 mA
2-4 kW
Flow: 2-4 m/s
Jet thickness: 1.5 mm
(~ 200°C)
neutron production
Ep= Ep_thresh = 1.880 MeV
power dissipation
by fast flow
Li flow: both neutron producing target and power dump
LiLiT: neutrons from 7Li(p,n) with a
mA-proton (kW) beam at SARAF I

## Slide 11: LiLiT at SARAF I beam corridor (1/2)
Beam
Beam
7Be cold trap
Oil heat exchanger

## Slide 12: LiLiT at SARAF I beam corridor (2/2)
Beam

## Slide 13: SARAF I - LiLiT nucleosynthesis research program
status | Collaboration HU-SARAF- | Detection technique | Target
M. Tessler et al., PLB 751 (2015) 418 | - | spec | natZr(n,g)
Under analysis | - | spec | natCe(n,g)
S. Pavetich et al., NIC 2016 | Goethe U Frankfurt –Dresden-Rossendorf-ANU | g spec + AMS | 23Na35,37Cl(n,g)
Under analysis | ANU-ANL | AMS | 92Zr(n,g)
L. Weissman et al., PRC 96 015802 (2017) | U. Seville | g spec | 208Pb(n,g)209Pb
A. Shor et al., PRC 96 055805 (2017) | JRC IRMM Geel | a + b + g spec | 209Bi(n,g)210gBi
Under analysis | ANL - Goethe U - U. Bern | g + b spec + MOT atom trap | natKr(n,g)
M. Tessler et al., PRL 121, 112701 (2018) | ANL - Goethe U | AMS + g spec | 36,38,40Ar(n,g)
M. Gai et al., Preliminary results | U Conn - PSI - CERN | CR-39 | 7Be(n,a)
C. Guerrero et al., submitted to PRL | U. Seville-PSI-CERN | spec | 171Tm(n,g)
C. Guerrero, ND2016 | U. Seville-PSI-CERN | spec | 147Pm(n,g)
Benchmark and higher precision
Noble gases
Radioactive
targets
Notes: 13

## Slide 14: Neutron θ=0° flux at SARAF I and II
Chart: neutron energy (keV)
I. Mardor et al., EPJA 54, 91 (2018)

## Slide 15: Spallation vs. stripping neutron spectra
40 MeV d-Li vs. 1400 MeV p-W, 0° spectra, 8 cm downstream the primary target
Spallation
Direct + stripping
T. Hirsh, WIS PhD Thesis 2012 D. Berkovits et al. LINAC 2012 I. Mardor et al., EPJA 2018
Area optimal for (n,a) (n,p) (n,2n) (n,f)
T. Stora et al., EPL, 98, 32001 (2012)
SARAF II - simulated
ISOLDE - measured

## Slide 16: The Science at SARAF (Phases I, II)
Searches for Beyond Standard Model Physics (abn of 6He, 23Ne, etc.)
Nuclear Astrophysics (s-process cross sections, r-process input)
Exploration of Exotic Nuclei (low z and fission products)
High Energy Deuteron and Neutron Induced Cross Sections (up to En ~ 50 MeV)
Material Research (Gen-IV, transmutation, fusion, blistering)
Neutron Based Therapy (Boron neutron capture therapy)
Development of New Radiopharmaceuticals (Diagnostics and Therapy)
Accelerator based neutron imaging (thermal and high energy)
Positron Annihilation Spectroscopy
And maybe also – neutrino physics (well-defined, pulsed, high energy, n and anti-n)
I. Mardor et al., "The Soreq Applied Research Accelerator Facility (SARAF) – Overview, Research Programs and Future Plans", Eur. Phys. Jour. A 54, 98 (2018)

## Slide 17: Fission fragments research potential at SARAF
n induced fission cross section at ~10 MeV is similar to p, d at ~20 MeV and higher
Advantage of neutron irradiation is the production of n-richer fission fragments
En ~ 10 MeV is optimal in terms of n-rich fission fragments versus prompt neutrons
Dmitry Gorelov, PhD thesis, U. Jyvaskyla, December 2015; D. Gorelov et al., NIM B376, 46 (2016)

## Slide 19: SARAF-II n-rich facility layout
Neutrons
Actinide
Deuteron beam
The combination of SARAF high power accelerator, LiLiT and FRS Ion Catcher may bring SARAF to be competitive with world planned facilities of n-rich exotic isotopes
S. Halfon et al., RSI 84, 123507 (2013)
W. R. Plass et al., NIM B 317 457 (2013)

## Slide 20: Conceptual layout for the SARAF Ion Catcher
Avoid neutron irradiation of instrumentation
Use next generation CSC design for FAIR:
He buffer gas density: ~0.2 mg/cm3
Fission product (FP) range in CSC: ~10 cm
Almost full stopping of FPs in CSC
CSC Extraction efficiency: 60%
RFQ Transmission: 90%
MR-TOF-MS efficiency: 50%
Detector efficiency / Transfer transmission to experiments: 80%
In following estimations: 1 thin target
T. Dickel et al.,
NIMB 376 216 (2016)
I. Mardor et al.,
EPJA 54, 91 (2018)
Liquid
Target jet

## Slide 21: Target Hall (2022)
 Phase-I accelerator
2001 2010
Reactor alternative 2014-2023
2014 2022
Phase-II accelerator
diffractometer
Radiopharmaceutical
Thermal n source
40 m
radiography
R&D
SARAF II 2023
Basic Research
Phase I Target Room
2016-2018
Fission
Fragment
Facility
Notes: 21

## Slide 22: Possible SARAF Fission Fragment Facility Layout Top View
1020
1309
Basement Level
300
270
Ground Level
RFQ beam line +
MR-ToF-MS (upright)
Ion Catcher control and power racks
RFQ beam line
Data, Power, vacuum, gas
Space and openings have been designed for installation of a CSC, RFQ beam line and MR-ToF-MS

## Slide 23
Ion Beam
450
300
Ground Level
GaIn jet
Possible SARAF Fission Fragment Facility Layout Side View
1309
570
Basement Level
CSC
RF carpet
Ion Catcher control and power racks
RFQ beam line
MR-ToF-MS
Data, Power, etc.
Space and openings have been designed for installation of a CSC, RFQ beam line and MR-ToF-MS

## Slide 24: Expected fission fragment rate from the SARAF II Liquid GaIn beam dump (1)
GaIn integral yield is ~0.5 of Li
GaIn angular distribution is less forward peaked than Li
(assume GaIn is similar to the measured Fe)
E. Eliyahu et al., SNRC Report 2019
M. Avrigeanu, V. Avrigeanu, private communication
M. Hagiwara et al. Fus. Sci. Tech., 48 1320 2005
T. Itoga et al., CYRIC Ann. Rep. 2004, 33

## Slide 25: Expected fission fragment rate from the SARAF II Liquid GaIn beam dump (2)
Setup may be improved by
  Increasing solid angle
  Optimizing actinide target angle w.r.t. beam
  Adding more actinide targets
Nevertheless, next slides use above estimate
Neutron energy [MeV]
Assume GaIn has similar n energy distribution as Fe

## Slide 26: SARAF II n-rich isotope production rates
SARAF-II isobarically separated isotopes in the experimental station, after MR-TOF-MS (isotopes/sec)
Based on 238U and 232Th targets (higher yield option per fission product)
Use En=14 MeV (n, fiss) cross sections (1.0 barn for 238U, 0.33 barn for 232Th)
Fission yields from JENDL FPY-2011 http://wwwndc.jaea.go.jp/cgi-bin/FPYfig?iso=nU238&eng=e2
r-process path (Sn ~ 3 MeV)
n drip line (Sn ~ 0)
~950 different fragments

## Slide 27: Handling of SARAF-II high rates at an ion catcher
~40 eV  1 He-e- pair
~100 MeV / FP  ~2×106 He-e- pairs / FP
~1010 FP/sec in buffer gas  ~2×1016 He-e- pairs/sec
~60% extraction efficiency for LEB design
Dedicated design for SARAF CSC could yield higher efficiency (also for higher rates)
Do not need/want to measure all FPs at once:
Degraders around actinide targets will suppress heavier FPs
Lower buffer gas pressure will suppress lighter FPs (will hit CSC walls)
Coarse mass filtering prior to high-resolving MR-TOF-MS mass measurements / filtering:
RFQ beam line – M/DM ~ 250 (~1u), 90% transmission, (~109 FP/sec)
MR-TOF-MS itself – M/DM ~ up to 70,000 (re-trapping schemes) (~107 FP/sec)
Detailed design and simulations needed to ensure full utilization of SARAF’s output

## Slide 28: Perspective – FRIB expected rates
B. Sherrill, Facility for Rare Isotope Beams, HRIBF Workshop (2009)
For all SARAF-II expected FPs, extracted FRIB rates from their online calculator:
‘Stopped beam’ rates
‘Ultimate FRIB yields’
‘FRIB Estimated Rates Version 1.08’, August 2017
Fission products cross sections from LISE++ 3EER Model
https://groups.nscl.msu.edu/frib/rates/fribrates.html
Plotted FPs for which R(SARAF-II) > R(FRIB)

## Slide 29: SARAF II / FRIB rates ratio
FPs for which R(SARAF-II) > R(FRIB)
FRIB rates are ‘stopped beam’
FRIB rates taken from ‘FRIB Estimated Rates Version 1.08’, August 2017 (‘Ultimate FRIB yields’) Fission products cross sections from LISE++ 3EER Model https://groups.nscl.msu.edu/frib/rates/fribrates.html
r-process path (Sn ~ 3 MeV)
n drip line (Sn ~ 0)
~270 different fragments

## Slide 30: Impact of nuclear properties on the r-process
Proton Number - Z
A. Aprahamian et al., Sensitivity studies for the main r process: nuclear masses, AIP Advances 4, 041101 (2014)

## Slide 31: Impact of nuclear properties on the r-process
Proton Number - Z
A. Aprahamian et al., Sensitivity studies for the main r process: nuclear masses, AIP Advances 4, 041101 (2014)

## Slide 32: Impact of nuclear properties on the r-process
Proton Number - Z
A. Aprahamian et al., Sensitivity studies for the main r process: nuclear masses, AIP Advances 4, 041101 (2014)

## Slide 33: Nuclear properties of n-rich isotopes at SARAF-II
Masses, Q-values, n-separation energies
Half lives
Mass and isotope fission fragment distributions
Fission fragment isomer ratios
g excitation levels
b-delayed neutron emission probabilities (Pn)
n spectra and energy levels
  Constraints on s(n,g) from  and/or neutron spectra
Spin, dipole and quadrupole moments
Mean-square charge radii
Array of n, b and g detectors such as
VANDLE
Versatile Array of Neutron Detectors at Low Energy
W. A. Peters et al., NIM A 836, 122-133 (2016)
Laser spectroscopy
such as in
IGISOL @ JYFL
A. R. Dicker et al., Hyp. Int. 227 139–145 (2014)

## Slide 34: Acknowledgements
This initiative is inspired by and based on: Leo Weissman & Michael Paul, Neutron-Rich Radioactive-Ion Production at SARAF Phase II, October 2013, internal report
Thanks for fruitful discussions with: SARAF Group (Soreq NRC), Michael Paul (HUJI), Eli Piasetzky (TAU), Ishay Pomerantz (TAU), Stephane Goriely (ULB), Gabriel Martinez-Pinedo (TUD), Wolfgang R. Plaß and the FRS Ion Catcher Collaboration, Iain Moore and the JYFL IGISOL Group, Paul Constantin and the ELI-NP RIB Group, Stephan Pomp

## Slide 35: Summary and Outlook
Soreq NRC is constructing SARAF as a versatile facility for the communities of applied and basic research and development
Scientific programs are ongoing at SARAF I, educating graduate students, and generating scientific results that are published and presented in international conferences
SARAF II is funded, to be completed at the first half of the next decade
Plans for SARAF II research programs are under development
The high neutron luminosity of SARAF + LiLiT and an Ion Catcher a la FRS, may constitute a world competitive facility for n-rich exotic isotopes research
Utilizing the SARAF II liquid GaIn beam dump may enable a realistic path towards the SARAF Fission Fragment Facility (no need for dedicated neutron source)
SARAF is open to new collaborators and contributions. We look forward to research proposals and letters of intent